Oklahoma’s Hazards: Dam Failures

As with any location in which man-made structures are built, potential failure of the structure could place lives and property at risk. During the past two years, at least 21 dam failures have occurred in the United States. The best way to minimize potential failure is to identify structures whose failure could cause the greatest loss of life and/or property, and to require those structures to undergo a rigorous inspection regime. Such is the case in Oklahoma. From a hazard management perspective, the most significant structures are those categorized as high-hazard dams. This designation relates solely to potential impacts of a structural breach; it is not an indication of the quality of construction or maintenance.

The Oklahoma Water Resources Board (OWRB) coordinates the Oklahoma Dam Safety Program to ensure the safety of more than 4,500 dams in the state which fall within its jurisdiction, especially those that could impact downstream life and property. Dams falling within the OWRB’s jurisdiction are non-federally constructed and maintained dams which are:  1) greater than 6 feet in height with storage capacities of 50 acre-feet or more; and/or 25 feet or greater in height with storage capacities of 15 acre-feet or more. The program requires inspections every five and three years for low and significant hazard structures, respectively. It requires annual inspection of the state's high-hazard dams, so designated due to the presence of one or more habitable structures downstream with loss of life likely to occur if a dam were to fail. There are 184 high-hazard dams in Oklahoma, which number includes federally constructed and maintained dams that are not regulated by the OWRB.

The Water Board requires submittal and subsequent approval of plans and specifications prior to dam construction or modifications to ensure the structures will meet minimum dam safety standards. OWRB staff also coordinates periodic training sessions and workshops on dam safety issues and regulations for dam owners and engineers. The Natural Resource Conservation Service offers technical assistance in the construction of small farm ponds and related structures.

These initial hazard classifications are based upon current conditions, including population and land-use patterns below the dams. Such conditions can  shift over time, such that a structure that is not considered high-hazard may receive such designation in the future, should, for example, dwellings be built within the floodplain below the dam. Other high-hazard dams may have such designation lowered should land-use patterns change, reducing the threat of loss to life or property. Mitigation aspects, such as relocations of vulnerable properties, can reduce the number and magnitude of high-hazard dams.

High-Hazard Dams in Oklahoma

The following map and listing of high-hazard dams in Oklahoma was provided by the Oklahoma Water Resources Board. Information is current as of April 2004.

| DAM NAME | COUNTY | NEAREST CITY | DISTANCE |
| --- | --- | --- | --- |
| SCS-Sallisaw Creek Site-15 | Adair | Bunch | 6 |
| SCS-Sallisaw Creek Site-16 | Adair | Bunch | 4 |
| SCS-Sallisaw Creek Site-17 | Adair | Bunch | 5 |
| SCS-Sallisaw Creek Site-18 | Adair | Bunch | 12 |
| SCS-Scraper Hollow Creek Site-2 | Adair | Proctor | 9 |
| Great Salt Plains Lake | Alfalfa | . | 1 |
| Atoka County Lake | Atoka | Fugate | 1 |
| Mcgee Creek Dike | Atoka | Negro Bend | 1 |
| SCS-Upper Elk Creek Site-22r | Beckham | Port | 17 |
| SCS-Upper Elk Creek Site-23a | Beckham | Elk City | 1 |
| SCS-Upper Elk Creek Site-23b | Beckham | Elk City | 2 |
| SCS-Upper Elk Creek Site-23c | Beckham | Elk City | 1 |
| Canton Lake | Blaine | Canton | 2 |
| Denison Dam | Bryan | Hendrix | 10 |
| Chickasha Lake | Caddo | Verden | 4 |
| Ft Cobb Lake | Caddo | Fort Cobb | 5 |
| DAM NAME | COUNTY | NEAREST CITY | DISTANCE |
| Southwestern Power Station No.3 | Caddo | Anadarko | 10 |
| Cedar Lake | Canadian | Norman | 38 |
| Northwood | Canadian | Oklahoma City | 0 |
| SCS-Cottonwood Creek Site-16 | Canadian | Cashion | 11 |
| SCS-Four Mile Creek Site-1 | Canadian | El Reno | 1 |
| SCS-Caddo Creek Site-18 | Carter | Ardmore | 5 |
| SCS-Caddo Creek Site-29 | Carter | Gene Autry | 1 |
| Hugo Lake | Choctaw | Sawyer | 0 |
| Lightning Creek Holding Pond A | Cleveland | Oklahoma City | 0 |
| Shadow | Cleveland | Moore | 0 |
| Stanley Draper | Cleveland | Oklahoma City | 0 |
| SCS-Caney-Coon-Creek Site-2 | Coal | Coalgate | 2 |
| 67th Street Reservoir | Comanche | . | 0 |
| Ellsworth | Comanche | Lawton | 12 |
| Elmer Thomas Lake | Comanche | Medicine Park | 1 |
| Lake George | Comanche | Lawton | 4 |
| Lawtonka Lake | Comanche | Medicine Park | 0 |
| Storm Detention Reservoir B-II | Comanche | . | 0 |
| Upper Canyon Lake | Comanche | Faxon | 18 |
| Walters City Lake | Cotton | Walters | 1 |
| Heyburn Lake | Creek | Kellyville | 2 |
| Lake Massena | Creek | Bristow | 1 |
| Parthenia Lake | Creek | Jenks | 6 |
| Sahoma Lake | Creek | Sapulpa | 2 |
| Sapulpa Lake | Creek | Sapulpa | 4 |
| SCS-Little Deep Fork Creek Site-33 | Creek | Bristow | 3 |
| Foss Reservoir | Custer | Clinton | 14 |
| SCS-Barnitz Creek Site-113 | Dewey | Clinton | 30 |
| SCS-Barnitz Creek Site-114 | Dewey | Clinton | 29 |
| SCS-Bear-Hybarger Site-3 | Garvin | Lindsay | 4 |
| SCS-Maysville Laterals Site-B3 | Garvin | Maysville | 1 |
| SCS-Wildhorse Creek Site-072 | Garvin | Davis | 7 |
| SCS-Wildhorse Creek Site-098 | Garvin | Foster | 0 |
| SCS-Wildhorse Creek Site-107 | Garvin | Elmore City | 0 |
| SCS-Bitter Creek Site-01 | Grady | Alex | 17 |
| SCS-Rush Creek Site-049 | Grady | Rush Spring | 1 |
| SCS-Winter Creek Site-02 | Grady | Alex | 7 |
| Timberlake | Grady | Norman | 25 |
| Altus North Dike | Greer | Blair | 4 |
| Stigler Lake | Haskell | Stigler | 3 |
| Holdenville City Lake | Hughes | Calvin | 12 |
| Waurika Lake | Jefferson | Waurika | 5 |
| Ponca | Kay | Ponca City | 1 |
| SCS-Uncle John Creek Site-02 | Kingfisher | Kingfisher | 6 |
| DAM NAME | COUNTY | NEAREST CITY | DISTANCE |
| Altus Auxiliary Dike | Kiowa | Blair | 4 |
| Altus East Dike | Kiowa | Lugert | 1 |
| Altus Lugert Dike | Kiowa | Lugert | 1 |
| Altus South Dike | Kiowa | Blair | 4 |
| Hunter | Kiowa | Hobart | 0 |
| Lake Altus | Kiowa | Blair | 7 |
| Carlton Lake | Latimer | Wilburton | 5 |
| SCS-Boiling Springs Site-1 | Latimer | Chilli | 1 |
| SCS-Fourche Maline Creek Site-01 | Latimer | Paonola | 1 |
| SCS-Fourche Maline Creek Site-04 | Latimer | Wilburton | 4 |
| SCS-Fourche Maline Creek Site-05 | Latimer | Wilburton | 6 |
| SCS-Fourche Maline Creek Site-07 | Latimer | Wilburton | 3 |
| SCS-Fourche Maline Creek Site-08 | Latimer | Panola | 5 |
| Robert S Kerr Lock And Dam 15 | Leflore | Redland | 7 |
| SCS-Caston Mountain Creek Site-5 | Leflore | Wister | 3 |
| SCS-Rock Creek Site-04 | Leflore | Talihina | 1 |
| W.D. Mayo Lock And Dam 14 | Leflore | Arkhoma | 9 |
| Wister Lake | Leflore | Poteau | 10 |
| Chandler City Lake | Lincoln | Chandler | 2 |
| SCS-Quapaw Creek Site-01 | Lincoln | Sparks | 0 |
| SCS-Quapaw Creek Site-15 | Lincoln | Meeker | 2 |
| Guthrie Country Club | Logan | Guthrie | 2 |
| Guthrie Lake | Logan | Guthrie | 4 |
| Liberty Lake | Logan | Guthrie | 7 |
| SCS-Cottonwood Creek Site-04 | Logan | Seward | 0 |
| SCS-Cottonwood Creek Site-11 | Logan | Seward | 10 |
| SCS-Fitzgerald-Soldier Creek Site-3M | Logan | Coyle | 4 |
| Madill City Lake | Marshall | Madill | 0.25 |
| Forebay | Mayes | Salina | 5 |
| Salina Dike | Mayes | Salina |  |
| Spavinaw | Mayes | Spavinaw | 0 |
| SCS-Criner Creek Site-003 | Mcclain | Payne | 5 |
| Broken Bow City Lake | Mccurtain | Broken Bow | 2 |
| Broken Bow Lake | Mccurtain | Eagletown | 2 |
| Pine Creek Lake | Mccurtain | Garvin | 20 |
| Eufaula Lake | Mcintosh | Whitefield | 6 |
| Arbuckle Dike 1 | Murray | Dougherty | 2 |
| Arbuckle Dike 2 | Murray | Dougherty | 2 |
| Arbuckle Lake | Murray | Gene Autry | 18 |
| Lacy | Murray | Sulphur | 0 |
| Webbers Falls Lock And Dam 16 | Muskogee | Webbers Falls | 5 |
| SCS-Stillwater Creek Site-40 | Noble | Stillwater | 7 |
| SCS-Upper Black Bear Creek Site-62 | Noble | Perry | 4 |
| SCS-Upper Black Bear Creek Site-64 | Noble | Perry | 3 |
| DAM NAME | COUNTY | NEAREST CITY | DISTANCE |
| Okemah Lake | Okfuskee | . | 5 |
| Weleetka | Okfuskee | Weleetka | 1 |
| Brixton Heights Addition | Oklahoma | Oklahoma City | 0 |
| Dry Creek Detention | Oklahoma | Oklahoma City | 0 |
| Hefner | Oklahoma | Oklahoma City | 0 |
| Knight | Oklahoma | Oklahoma City | 0 |
| Lightning Creek Holding Pond C | Oklahoma | Oklahoma City | 0 |
| Northeast | Oklahoma | Oklahoma City | 0 |
| NW Oklahoma City Sludge Lagoon No 1 | Oklahoma | Oklahoma City | 0 |
| Overholser | Oklahoma | Oklahoma City | 0 |
| Regal | Oklahoma | Oklahoma City | 0 |
| Ski Island Lake | Oklahoma | Oklahoma City | 0 |
| Twin Lakes 0west | Oklahoma | Oklahoma City | 0 |
| Twin Lakes East | Oklahoma | Oklahoma City | 0 |
| Will Rogers Park Holding Pond | Oklahoma | Oklahoma City | 0 |
| Henryetta | Okmulgee | Four Corners | 2 |
| Nichols | Okmulgee | Henryetta | 2 |
| Okmulgee Lake | Okmulgee | Schulter | 7 |
| SCS-Okmulgee Creek Site-1 | Okmulgee | Okmulgee | 2 |
| SCS-Okmulgee Creek Site-2 | Okmulgee | Okmulgee | 1 |
| Birch Lake | Osage | Avant | 13 |
| Bluestem | Osage | Pawhuska | 4 |
| Deer Lake | Osage | Bartlesville | 16 |
| Fairfax | Osage | Fairfax | 2 |
| Hominy Lake | Osage | Hominy | 1 |
| Hudson Lake | Osage | Bartlesville | 5 |
| Hulah Lake | Osage | Bartlesville | 15 |
| Kaw Lake | Osage | Ponca City | 8 |
| Pawhuska | Osage | Pawhuska | 3 |
| Shell | Osage | Wekiwa | 2 |
| Waxhoma | Osage | Barnsdall | 3 |
| Pawnee Lake | Pawnee | Pawnee | 1 |
| SCS-Lower Black Bear Creek Site-17 | Pawnee | Pawnee | 1 |
| Carl Blackwell Lake | Payne | Stillwater | 6 |
| Cedar Isle | Payne | Stillwater | 1 |
| Cushing Lake | Payne | Cushing | 5 |
| SCS-Stillwater Creek | Payne | Stillwater | 1 |
| SCS-Stillwater Creek Site-23 | Payne | Stillwater | 0 |
| SCS-Stillwater Creek Site-24 | Payne | Stillwater | 3 |
| SCS-Stillwater Creek Site-28 | Payne | Stillwater | 1 |
| SCS-Stillwater Creek Site-29 | Payne | Stillwater | 1 |
| SCS-Stillwater Creek Site-30 | Payne | Stillwater | 0 |
| SCS-Stillwater Creek Site-46 | Payne | Stillwater | 5 |
| Pittsburg | Pittsburg | Pittsburg | 2 |
| DAM NAME | COUNTY | NEAREST CITY | DISTANCE |
| SCS-Sandy Creek Site-01 | Pontotoc | Ada | 4 |
| SCS-Sandy Creek Site-18 | Pontotoc | Vanoss | 2 |
| SCS-Upper Clear Boggy Creek Site-33 | Pontotoc | Ahloso | 3 |
| SCS-Upper Clear Boggy Creek Site-34 | Pontotoc | Ahloso | 3 |
| Shawnee City No.1 | Pottawatomie | Shawnee | 8 |
| Shawnee City No.2 | Pottawatomie | Shawnee | 8 |
| Tecumseh | Pottawatomie | Shawnee | 4 |
| Clayton Lake | Pushmataha | Clayton | 2 |
| SCS-Sargeant Major Creek Site-2 | Roger Mills | Cheyenne | 2 |
| Claremore Lake | Rogers | Claremore | 1 |
| Oologah Lake | Rogers | Catoosa | 12 |
| SCS-Big Wewoka Creek Site-22 | Seminole | Wewoka | 5 |
| Wewoka | Seminole | Wewoka | 3 |
| Muldrow Lake | Sequoyah | Muldrow | 4 |
| SCS-Sallisaw Creek Site-28 | Sequoyah | Marble City | 2 |
| SCS-Sallisaw Creek Site-32 | Sequoyah | Sallisaw | 3 |
| SCS-Sallisaw Creek Site-33 | Sequoyah | Sallisaw | 3 |
| Comanche | Stephens | Courtney | 36 |
| SCS-Cow Creek Site-25A | Stephens | Comanche | 1 |
| Optima Lake | Texas | Beaver | 32 |
| A.B. Jewell | Tulsa | . | 0 |
| Keystone Lake | Tulsa | Sand Springs | 5 |
| Warrenton Lake | Tulsa | Tulsa | 0 |
| Yahola | Tulsa | Tulsa | 0 |
| Chouteau Lock And Dam 17 | Wagoner | Okay | 2 |
| Fort Gibson Lake | Wagoner | Fort Gibson | 5 |
| Newt Graham Lock And Dam 18 | Wagoner | Okay | 25 |
| Bar-Dew | Washington | Bartlesville | 4 |
| SCS-Double Creek Site-1 | Washington | Ramona | 3 |
| Clinton | Washita | Foss | 3 |
| Hobart | Washita | Rocky | 1 |
| SCS-Cavalry Creek Site-24 | Washita | Cordell | 1 |
| SCS-Cobb Creek Site-002 | Washita | Colony | 3 |
| SCS-Cobb Creek Site-003 | Washita | Colony | 3 |
| SCS-Cobb Creek Site-01 | Washita | Colony | 5 |
| Fort Supply Lake | Woodward | Fort Supply | 1 |

OKLAHOMA WATER RESOURCES BOARD

PLANNING & MANAGEMENT DIVISION

DAM INSPECTION CHECKLIST

NAME OF DAM ____________________________	COUNTY ____________________________

OWNER & ADDRESS _______________________	OWNER APPLICATION # _______________

_________________________________________	OWNER PLAN # ______________________

_________________________________________	IDENTIFICATION # ____________________

PURPOSE OF DAM_________________________	INSPECTED BY _______________________

LEGAL section_____ township______ range______	HAZARD CLASS ______________________

WEATHER ________________________________	INSPECTION DATE ____________________

| ITEM | Y | N | N/A | REMARKS |
| --- | --- | --- | --- | --- |
| 1. General Conditions |  |  |  |  |
| a. Alterations to dam? |  |  |  |  |
| b. Development in downstream floodplain? |  |  |  |  |
| C. Grass cover adequate? |  |  |  |  |
| D. Settlements, misalignments or cracks? |  |  |  |  |
| E. Recent high water marks |  |  |  | elevation |
| 2. Upstream Slope |  |  |  |  |
| A. Erosion? |  |  |  |  |
| B. Trees? |  |  |  |  |
| C. Rodent holes? |  |  |  |  |
| D. Cracks, settlements or bulges? |  |  |  |  |
| E. Adequate and sound rip rap? |  |  |  |  |
| 3. Intake Structure concrete [ ] metal [ ] |  |  |  | water surface elevation |
| A. Spalling, cracking, scaling? |  |  |  |  |
| B. Exposed reinforcement? |  |  |  |  |
| C. Corrosion present? |  |  |  |  |
| D. Coating adequate? |  |  |  |  |
| E. Leakage? |  |  |  |  |
| F. Trash rack adequate? |  |  |  |  |
| G. Obstacles to inlet? |  |  |  |  |
| H. Drawdown operative? Closed [ ] Open [ ] |  |  |  |  |
| 4. Abutment Contacts |  |  |  |  |
| A. Erosion, cracks or slides? |  |  |  |  |
| B. Seepage? |  |  |  | estimated gpm |
| 5. Emergency Spillway |  |  |  |  |
| A. Obstructions? |  |  |  |  |
| B. Erosion? |  |  |  |  |
| C. Rodent holes? |  |  |  |  |
| 6. Downstream Slope |  |  |  |  |
| A. Erosion? |  |  |  |  |
| B. Trees? |  |  |  |  |
| C. Rodent holes? |  |  |  |  |
| D. Cracks, settlements, bulges? |  |  |  |  |
| E. Drains or wells flowing? |  |  |  | estimated gpm |
| F. Seepage or boils? |  |  |  | estimated gpm |

| ITEM | Y | N | N/A | REMARKS |
| --- | --- | --- | --- | --- |
| 7. Conduit & Outlet concrete [ ] metal [ ] |  |  |  | tailwater elevation/flow |
| A. Spalling, cracking, scaling? |  |  |  |  |
| B. Exposed reinforcement? |  |  |  |  |
| C. Joints displaced or offset? |  |  |  |  |
| D. Joint material lost? |  |  |  |  |
| E. Leakage? |  |  |  |  |
| F. Earth erosion? |  |  |  |  |
| G. Conduit misaligned? |  |  |  |  |
| H. Outlet channel obstructed? |  |  |  |  |
| 8. Stilling Basin |  |  |  |  |
| A. Spalling, cracking, scaling? |  |  |  |  |
| B. Exposed reinforcement? |  |  |  |  |
| C. Joints displaced or offset? |  |  |  |  |
| D. Joint material lost? |  |  |  |  |
| E. Joints leak? |  |  |  |  |
| F. Rock adequate? |  |  |  |  |
| G. Dissipater deteriorating? |  |  |  |  |
| H. Dissipater clean of debris? |  |  |  |  |
| 9. Concrete Spillway |  |  |  |  |
| A. Spalling, cracking, scaling? |  |  |  |  |
| B. Exposed reinforcement? |  |  |  |  |
| C. Joints displaced or offset? |  |  |  |  |
| D. Joint material lost? |  |  |  |  |
| E. Leakage? |  |  |  |  |
| F. Dissipater deteriorating? |  |  |  |  |
| G. Dissipater clean of debris? |  |  |  |  |
| H. Earth erosion? |  |  |  |  |
| I. Outlet channel eroding? |  |  |  |  |
| 10. Gates |  |  |  |  |
| A. Floodgates broken or bent? |  |  |  |  |
| B. Floodgates eroded or rusted? |  |  |  |  |
| C. Floodgates operational? |  |  |  |  |
| 11. Reservoir |  |  |  |  |
| A. Developed? |  |  |  |  |
| B. Slides or erosion on banks? |  |  |  |  |
| C. Reservoir managed? |  |  |  |  |
| 12. Instruments |  |  |  |  |
| A. Structure instrumented? |  |  |  |  |
| B. Monitoring performed? |  |  |  |  |
| **Reevaluate Hazard Classification |  |  |  |  |
| REMARKS: |  |  |  |  |

NAME OF ENGINEER _________________________________________

DATE ______________________________________________________

ENGINEERING FIRM __________________________________________

OR GOVERNMENT AGENCY____________________________________

SIGNATURE _________________________________________________

PROFESSIONAL ENGINEER SEAL