## Floods and Flash Floods: Hazards in Oklahoma

Nationally, flooding and flash flooding is the number one killer of all storm-related natural disasters. An average of about 140 people die each year in the United States due to flooding and flash flooding.  In Oklahoma, flash flooding is a consistent threat to life.

This document will focus on flooding caused by excessive precipitation.  Flooding as a result of large structural failures will be treated in a separate document.

# Definitions: Flash Flooding versus River Flooding

Flooding occurs on continuous scales of time and area. Humans tend to group events into two categories: flash flooding and river flooding. Flash flooding refers to events that occur during or immediately after the life cycle of a thunderstorm.  These events respond on the order of minutes to hours to heavy precipitation.  River flooding refers to the response of larger streams to prolonged precipitation. Flooding on this scale may take days, or even weeks, to culminate.

Vulnerability to flash flooding and river flooding is a dichotomy, in that flash flooding’s primary threat is to human life and safety, while river flooding’s primary threat is substantial economic damage.

The size of a stream’s watershed is the dominant factor in the time scale of its response to heavy precipitation.  For example, very small creeks and branches of creeks can respond in minutes to heavy precipitation.  Larger rivers, such as the Arkansas, may take days to crest after prolonged periods of rainfall.

| Characteristic or Factor | Flash Flooding | River Flooding |
| --- | --- | --- |
| Size of waterway | Small (from unnamed creeks to larger creeks) | Large creeks, minor rivers, major rivers |
| Area of watershed or catchment | Several hundred acres to tens of square miles | About a hundred to several thousand square miles |
| Associated precipitation | Convective storms, often slow-moving or “training” thunderstorms | Larger-scale precipitation patterns, often slow-moving fronts or remnants of tropical storms, or both |
| Duration of event | Minutes to hours | Hours to days |
| Time scale of response | Minutes to hours | Hours to days |
| Warning Lead Time | Short (no warning to several minutes) | Significant (several hours to about a day) |
| Location of flooding | Within or very near the footprint of heavy rainfall | Often downstream of heavy rainfall (increasingly so with larger watersheds) |
| Primary threat | Loss of life; human safety | Loss of property; economic disruption |
| Table A. Typical characteristics of, and factors related to, flash flooding and river flooding in Oklahoma. |

# Flash Flooding

Flash flooding occurs when the precipitation rate becomes so large that waterways cannot evacuate the runoff, streams swell and flash flooding occurs. It can occur as soon as minutes after a downpour has begun. The conditions that lead to flash flooding can happen anywhere in Oklahoma, during any season, and at any time of day.

Flash flooding is a real and significant hazard to life in Oklahoma because of two major factors:

- The prevalence of convective precipitation. Thundershowers and thunderstorms can produce precipitation at very high rates.  These events are certainly a large part of Oklahoma’s rainfall climate.  They are especially prevalent during the warm season.

- Vehicular travel.

People often underestimate the power of water. This leads to many unfortunate and sometimes tragic encounters during seemingly minor flooding events. As little as six inches of water can cause a driver to lose control of a passenger vehicle.

From 1960-2002, there were 94 deaths due to flash flooding in Oklahoma.  The vast majority of these deaths are vehicle-related. Since 1994, all flash flood deaths in Oklahoma have been vehicle-related.

| Factor | Effect |
| --- | --- |
| Precipitation Rate | The most obvious contributing factor. As the rate of precipitation increases, so to does its ability to outpace the ability of the watershed to absorb it. This is the dominant factor in flash flooding events, and can overwhelm any or all of the following factors. |
| Training Echoes | Storm cells that follow each other (much like box cars on a train) can repeatedly deposit large amounts of water on the same watershed, overwhelming its ability to handle runoff. |
| Slope of Watershed | Steeper topography (hills, canyons, etc.) will move runoff into waterways more quickly, resulting in a quicker, flashier response to precipitation. |
| Shape of Watershed | Longer, narrower watersheds will tend to “meter out” runoff so that water arrives from downshed (nearer to the mouth of the stream) areas faster than from upshed areas. In watersheds that are more square or circular than elongated, runoff tends to arrive in the main stem at the same time, intensifying the response. This factor becomes more significant with larger watersheds. |
| Saturation of Soils | Saturated or near-saturated soils can greatly reduce the rate at which water can soak into the ground. This can increase runoff dramatically. |
| Hardened Soils | Extremely dry soils can develop a pavement or “crust” that can be resistant to infiltration. This is especially true in areas of recent wildfire, where plant oils or resins may cause the soil to be even more water-resistant. |
| Urbanization | The urban environment usually intensifies the response to heavy precipitation. The two dominant urban factors are: 1) increased pavement coverage, which prevents infiltration and dramatically increases runoff; and 2) Urban systems are designed to remove water from streets and byways as quickly as possible. This accelerates the natural response to precipitation by placing runoff in waterways much more quickly. |
| Low-water crossings | The vast majority of flash-flood related deaths occur in vehicles. Many of these deaths occur at low-water crossings where the driver is unaware of the depth of the water or the consequences of driving into it. |
| Table B. Contributing factors to flash-flood hazard and vulnerability in Oklahoma. |

Figure 1. Flood and flash-flood related deaths in Oklahoma and nearby states, 1961-1999. Single events strongly influenced totals in Colorado (Big Thompson, 1976, 140 deaths), Louisiana (Hurricane Betsy, 1965, 50+ deaths), and Mississippi (Hurricane Camille, 1969, ~130 deaths).

Figure 2. Flood-related deaths in Oklahoma by year since 1960. The vast majority of these deaths are flash flood deaths, and the vast majority of those are vehicle-related.

# River Flooding

Flooding of larger streams and rivers typically requires many hours (a day or more) of intermittent or continuous heavy precipitation over a larger area. Typical scenarios for river flooding may involve a stalled or slow-moving front with persistent associated precipitation, the remnants of a land-falling tropical storm, or interaction between these two features.

River flooding occurs when heavy runoff from several tributaries converge in a larger stream’s main channel.  The stream level rises, crests and drops over the course of hours or days.  As a general rule of thumb, the response to precipitation is slower for larger rivers. River flood damage occurs over a wide area, sometimes several square miles.

Oklahoma’s vulnerability to river flooding changed dramatically during the last half of the 20th Century.  Several factors combined to minimize the loss of life due to river flooding:

- Physical Floodwater Control – Widespread damming of rivers and upstream tributaries has dramatically reduced the frequency and magnitude of river flooding in Oklahoma.

- More Accurate Forecasting – Hydrological forecasting has improved, as has the timeliness and availability of rainfall observations. As a result, the forecast level of larger streams is much more predictable. River stage forecasting has matured to levels of accuracy that were impossible early in the century.

- Longer Warning Lead-Times – Because river flooding typically occurs hours to days after rainfall ceases, warnings for river flooding often provide much more lead time than those for flash flooding.

- Floodplain Management – The state, through the Oklahoma Water Resources Board, has aggressively pursued a policy of mitigation through incremental reclamation of flood-prone areas. This has gradually reduced the number of residences in harm’s way.

As a result of these factors, the primary vulnerability to river flooding is economic in nature. Most major economic damage is confined to a few very large events.  For example, flooding during the three years of 1957, 1984 and 1986 caused more damage than the remainder of the years between 1955-1999 (see Figure 3).

Figure 3. Economic damage due to flooding in Oklahoma: 1955-1999. River flooding events in 1957, 1984 and 1986 constitute the majority of dollars during the period. From Climatological Data National Summary, Annual Summary 27(13), 124; U.S. Army Corps of Engineers (1992) and (1999).

# Seasonal Trends in River Flooding

Spring and fall are the preferred seasons for river flooding, because these are the seasons that provide the bulk of Oklahoma’s rainfall. However, river flooding can occur during any month on the calendar.

Autumn months in Oklahoma provide an enhanced threat of wide-scale flooding because of the combination of several contributing factors. Late summer and autumn are the peak of the Gulf hurricane/tropical storm season. Large-scale weather patterns (fronts and upper-level storms) are also much more active in the autumn than in the summer. Moisture from landfalling tropical storms can interact with slow-moving fronts to provide heavy rains for days at a time.  In Oklahoma, these are the ingredients for river flooding. The moisture can be provided by tropical storms in the Gulf of Mexico, or even from the remnants of Pacific tropical storms (see Table C).

| Year | Month | Tropical Storm | Source Region | Comments |
| --- | --- | --- | --- | --- |
| 1996 | September | Fausto | Pacific | 6+ inches rain; minor flooding along North Canadian. |
| 1995 | August | Dean | Gulf of Mexico | 12-16 inches in parts of OK; interacted with weak, stalled cold front; major flooding along much of Salt Fork of the Arkansas River in Grant and Kay Counties; flooding also occurred on Cimarron, Washita and Arkansas Rivers. |
| 1988 | September | Gilbert | Gulf of Mexico | Interaction with slow-moving front; 4+ inch rains fell onto saturated soils; flooding on creeks and rivers. |
| 1986 | September-October | Paine | Pacific | Up to 20 inches in north-central OK; massive flooding on Cimarron. flooding on the Arkansas River; ground was already saturated by rainfall associated with remnants of Pacific Hurricane Newton; estimated damages of $350 million; 52 counties declared disaster areas. |
| 1983 | October | Tico | Pacific | Up to 17 inches rain in southwest and central OK; Red River at Burkburnett and Terral rose to highest stage in 60 years; widespread flooding of smaller rivers and creeks. |
| 1981 | October | Norma | Pacific | Up to 24 inches of rain in south-central OK (Monthly total of 25.8” at Madill is greatest for any station during any month in OK history). |
| 1961 | September | Carla | Gulf of Mexico |  |
| Table C. Selected Tropical-Storm-Related River Flooding in Oklahoma. |

Appendix A: Oklahoma Flash-Flood Warnings and Events, 1986-2003

The following list contains the total number of flash flood warnings and verified flash flood events for each of Oklahoma’s 77 counties.  Warnings indicate the number of times that meteorological conditions indicated an imminent threat of flash flooding.  Verified events are the number of flash flood events that were confirmed by National Weather Service (NWS) personnel in follow-up investigations.

Discrepancies between the two sets of numbers are indicative that not all flash-flood events receive warnings, and not all warnings have subsequent flooding. Flash flood forecasting is difficult and limited somewhat by observational technology. Flash flood events in sparsely populated areas are more difficult to verify than those in urban areas. During times of widespread severe weather, flash flooding is only one of several hazards that threaten the public, and must “compete” with violent weather for the time and attention of NWS staff.

| County | Warnings Issued | Verified Events |
| --- | --- | --- |
| Adair | 33 | 19 |
| Alfalfa | 31 | 22 |
| Atoka | 32 | 15 |
| Beaver | 11 | 4 |
| Beckham | 18 | 5 |
| Blaine | 21 | 10 |
| Bryan | 57 | 26 |
| Caddo | 40 | 19 |
| Canadian | 49 | 20 |
| Carter | 32 | 14 |
| Cherokee | 46 | 34 |
| Choctaw | 38 | 16 |
| Cimarron | 9 | 10 |
| Cleveland | 37 | 25 |
| Coal | 17 | 5 |
| Comanche | 44 | 30 |
| Cotton | 30 | 12 |
| Craig | 27 | 20 |
| Creek | 49 | 42 |
| Custer | 18 | 10 |
| Delaware | 21 | 18 |
| Dewey | 13 | 6 |
| Ellis | 16 | 7 |
| Garfield | 36 | 21 |
| Garvin | 17 | 9 |
| Grady | 49 | 13 |
| Grant | 41 | 26 |
| Greer | 23 | 8 |
| Harmon | 14 | 8 |
| Harper | 7 | 3 |
| Haskell | 31 | 24 |
| Hughes | 12 | 5 |
| Jackson | 32 | 15 |
| Jefferson | 29 | 13 |
| Johnston | 25 | 9 |
| Kay | 63 | 46 |
| Kingfisher | 45 | 21 |
| Kiowa | 37 | 16 |
| Latimer | 45 | 32 |
| Le Flore | 71 | 36 |
| Lincoln | 26 | 18 |
| Logan | 4 | 21 |
| Love | 26 | 6 |
| Major | 17 | 10 |
| Marshall | 33 | 13 |
| Mayes | 26 | 15 |
| McClain | 30 | 8 |
| McCurtain | 71 | 29 |
| McIntosh | 28 | 21 |
| Murray | 26 | 16 |
| Muskogee | 48 | 33 |
| Noble | 26 | 12 |
| Nowata | 31 | 25 |
| Okfuskee | 20 | 17 |
| Oklahoma | 65 | 49 |
| Okmulgee | 38 | 32 |
| Osage | 71 | 54 |
| Ottawa | 23 | 18 |
| Pawnee | 37 | 21 |
| Payne | 20 | 12 |
| Pittsburg | 52 | 39 |
| Pontotoc | 17 | 5 |
| Pottawatomie | 22 | 13 |
| Pushmataha | 48 | 18 |
| Roger Mills | 11 | 4 |
| Rogers | 44 | 38 |
| Seminole | 16 | 11 |
| Sequoyah | 34 | 20 |
| Stephens | 44 | 31 |
| Texas | 13 | 8 |
| Tillman | 30 | 14 |
| Tulsa | 74 | 61 |
| Wagoner | 38 | 27 |
| Washington | 29 | 27 |
| Washita | 19 | 11 |
| Woods | 14 | 11 |
| Woodward | 14 | 8 |
| Statewide | 2495 | 1470 |